## Slide 1: Сетевые технологии.
TCP/IP
TCP UDP NAT Firewall

## Slide 2
Wikipedia
Transmission Control Protocol (TCP, протокол управления передачей) — один из основных протоколов передачи данных интернета, предназначенный для управления передачей данных. Пакеты в TCP называются сегментами.

## Slide 3
Wikipedia
UDP (англ. User Datagram Protocol — протокол пользовательских датаграмм) — один из ключевых элементов набора сетевых протоколов для Интернета. С UDP компьютерные приложения могут посылать сообщения (в данном случае называемые датаграммами) другим хостам по IP-сети без необходимости предварительного сообщения для установки специальных каналов передачи или путей данных.

## Slide 4
Socket
A network socket is a software structure within a network node of a computer network that serves as an endpoint for sending and receiving data across the network. The structure and properties of a socket are defined by an application programming interface (API) for the networking architecture. Sockets are created only during the lifetime of a process of an application running in the node.

## Slide 5
Port
In computer networking, a port is a communication endpoint. At the software level, within an operating system, a port is a logical construct that identifies a specific process or a type of network service. A port is identified for each transport protocol and address combination by a 16-bit unsigned number, known as the port number. The most common transport protocols that use port numbers are the Transmission Control Protocol(TCP) and the User Datagram Protocol (UDP).

## Slide 6
Sockets, ports.
Well known ports: 1-1023
Registered ports: 1024-49151
Dynamic, private or ephemeral ports: 49152-65535

## Slide 7
TCP UDP
Protocol | TCP | UDP
Connection | Established SYN, ACK, FIN | Connectionless
Usage | High reliability | Efficient Transmission, Huge number of clients
Ordering of data | Rearranges packets in order | no order
Reliability | yes | no
Streaming | Byte stream with congestion control | Individual datagrams
Error Checking | error checking and recovery | checksum - drop datagrams if error
Acknowledgement | Segments acknowledgements | -

## Slide 8
TCP UDP

## Slide 9
TCP sockets

## Slide 10
UDP sockets

## Slide 11
NAT
Network address translation (NAT) is a method of remapping an IP address space into another by modifying network address information in the IP header of packets while they are in transit across a traffic routing device.[1] The technique was originally used to avoid the need to assign a new address to every host when a network was moved, or when the upstream Internet service provider was replaced, but could not route the networks address space. It has become a popular and essential tool in conserving global address space in the face of IPv4 address exhaustion. One Internet-routable IP address of a NAT gateway can be used for an entire private network.

## Slide 12
NAT

## Slide 13
NAT

## Slide 14
NAT PAT

## Slide 15
NAT

## Slide 16
NAT

## Slide 17
IP routing table:
http://jodies.de/ipcalc

## Slide 18
Inter-vlan routing.